## Slide 1: Electrical Circuits EEE 1131

## Slide 2
Course Teacher
মোঃ সাফিউল ইসলাম
Assistant Professor, Dept. of EEE, KUET
Email: shafiul.islam41@gmail.com

## Slide 3: Syllabus

## Slide 4: Syllabus

## Slide 5: Introduction
Topics:
Network terminology
Voltage
Current
Independent and Dependent sources

## Slide 6: Cont.
Resistance
Basic laws
Ohm’s Law
KVL
KCL

## Slide 7: Cont.
Simple resistive circuit
Series and parallel circuits
Voltage and current division
Wye-Delta transformation

## Slide 8: Commonly used network terminology
Circuit
Branch
Node or Junction point
Loop
Mesh

## Slide 9: Circuit
A closed Conducting path through which a current flows or intended to flow.

## Slide 10: Branch
Any two terminal element in a electrical circuit or network is called a branch.
Ex. Resistor, inductor, capacitor, source, e.t.c.
How many branches are there in the circuit shown in left side?
1
2
1
2
1
2
1
2

## Slide 11: Node or Junction
A node or junction is a point where at least two or more branches are connected together.
“KCL is applicable only at node or junction point”
How many node are there in the circuit?

## Slide 12: Node or Junction
4 Nodes
1
2
3
4

## Slide 13: Loop
A loop is a closed path formed by starting from a node and passing through a sets of node and returning back to the starting node without passing through any node more than once is called a loop.

## Slide 14: Mesh
A Mesh is special type of loop that does not contains any other loop within it.
“KVL is applicable around any mesh or closed path”

## Slide 15: Loop and Mesh
1
2
3
4

## Slide 16: Voltage
Voltage (or potential difference) is the energy required to move a unit
charge through an element, measured in volts (V)

## Slide 17: Voltage
The voltage between two points a and b in an electric circuit is the energy (or work) needed to move a unit charge from a to b; mathematically,

## Slide 18: Voltage
Voltage at point a is +9V more than b
Or
voltage at point b is -9V more than a

## Slide 19: Voltage
Potential rise from point b to a is +9V
And
Potential drop from point b to a is -9V

## Slide 20: Voltage
Suppose you put a kick on a football
The football gets motion due to your kick
So kick is the cause and the motion of the football is effect kick---cause and
Motion of the football---effect
Similarly, Voltage is the cause and flow or displacement of charge (current) is effect

## Slide 21: Current
Due to voltage or potential drop charge flow through the element.
And the rate of change of charge w.r.t time, t is called current.
Electric current is the time rate of change of charge, measured in
amperes (A). Mathematically,

## Slide 22: Classification Current
Two types
Direct Current (DC)
Alternating Current (AC)

## Slide 23: Direct Current
DC current is a current that remains constant with time.
By convention, the uppercase letters are used to represent DC quantities.

## Slide 24: Alternating Current
An AC current is a current that varies sinusoidally with time.
By convention, the lowercase letters are used to represent AC quantities.

## Slide 25: Direction of Current
We are defining the current as time rate of change of charge.
Conventionally,
Direction of current flow is taken opposite to the direction of flow of negative charge i.e., electron flow direction
Direction of current flow

## Slide 26: Cont.

## Slide 27: Summary
Voltage is the energy or work needed to move a unit charge through an element.
Current is the time rate of change of charge due to the application of voltage.

## Slide 28: Cont.
Voltage or potential difference or potential drop is always across the element or between two points.
But
Current is always through the element.

## Slide 29: Voltage
Voltage is a point function. It is measured from a reference point. We measure voltage of any point w.r.t. a reference point called ground. The potential of ground is 0 V.

## Slide 30: Single subscript notation
Potential of point a, w.r.t. ground or reference point is, Va0
Potential of point b, w.r.t. ground or reference point is, Vb0
Va0 and Vb0 are sometimes denoted as simply Va or Vb instead of Va0 or Vb0
a
b
c
0
0 V

## Slide 31: Single subscript notation
Voltage drop across resistor, R1=Vab
Vab=Va0-Vb0=Va-Vb
Vab is also called as voltage or potential difference between point a and b
a
b
c
0
0 V
R1
R2
R3

## Slide 32: Circuit Elements
Active elements
Passive elements
“An active element is capable of
generating energy while a passive element is not”

## Slide 33: Circuit Elements
Active elements-Battery, Operational amplifier, Generator, Voltage source, current source
Passive elements-Resistors, inductors, capacitors

## Slide 34: Active Elements
Two most common and important active elements are voltage source and current source
In a word “Source”
Two types
Independent sources
Dependent sources

## Slide 35: Independent Sources
An ideal independent source is an active element that provides a specified voltage or current that is completely independent of other circuit elements .
Independent Voltage source
Independent current source

## Slide 36: Dependent Sources
An ideal dependent (or controlled) source is an active element in which the source quantity is controlled by another voltage or current .
Dependent Voltage Source
Dependent Current Source

## Slide 37: Dependent Sources
It may be either a voltage source or current source.
And it’s quantity can be controlled by either (another)voltage or current.
2 types or source and 2 type of controlling parameter, that’s why there are 4 possible dependent sources.

## Slide 38: Dependent Sources
Voltage-controlled voltage source(VCVS)
Voltage-controlled current source (VCCS)
Current-controlled voltage source (CCVS)
Current-controlled current source (CCCS)

## Slide 39: Dependent Sources

## Slide 40: Resistance
The physical property, or ability
of a material to resist current, is
known as resistance and is
represented by the symbol R.
R=Resistance, ohm
A=Cross-sectional area in m2
=resistivity in ohm-m

## Slide 41: Basic Laws
Ohm’s Law
Kirchhoff’s Voltage Law (KVL)
Kirchhoff’s Current Law (KCL)

## Slide 42: Ohm’s Law
Ohm’s law states that the current i flowing through the resistor is directly proportional to the voltage v across a resistor at a fixed temperature.
G-Conductance and opposite to resistance, R.

## Slide 43: Ohm’s Law
i
v
Slope=1/R
v
Slope=1/R
Graphical Representation of Ohms law
Linear Resistor
nonlinear Resistor

## Slide 44: Two extreme possible value of R
Open Circuit (R tends to infinity)
Short Circuit (R tends to zero)

## Slide 45: Open Circuit
An open circuit is a circuit element with resistance approaching infinity.

## Slide 46: Short Circuit
A short circuit is a circuit element with resistance approaching zero.

## Slide 47: Classification of Resistors
Fixed Resistors
Variable Resistors
Wire wound type
Carbon film type
Fixed
Variable Resistor

## Slide 48: Kirchhoff’s Voltage Law (KVL)
Kirchhoff’s voltage law (KVL) states that the algebraic sum of all voltages around a closed path (or loop) is zero Voltage rise + ve
Voltage drop- ve

## Slide 49: Kirchhoff’s Voltage Law (KVL)
“KVL is applicable only around a closed path or loop”

## Slide 50: KVL
“Current entering point of an element is at higher potential than current leaving point of that element”

## Slide 51: KVL
V1+V4=V2+V3+V5
V1-V2-V3+V4-V5=0
Sum of potential rises
Sum of potential drops
Algebraic sum of potentials
around a closed path

## Slide 52: KCL
Algebraic sum of current entering and leaving at the same junction is equal to zero.
sum of Entering currents=sum of leaving currents
I1+i3+i4=i2+i5
The sum of the currents entering a node is equal to the sum of the currents leaving the node

## Slide 53: Series circuit and Voltage division
Let the current I
So V1=i*R1
V2=i*R2
Applying KVL,
V-V1-V2=0 or V=V1+V2 =i*(R1+R2)
i=V/(R1+R2)=V/Req
Therefore, Req=R1+R2
1
2
1
2
1
2

## Slide 54: Series circuit and Voltage division
Req=R1+R2
two resistors can be replaced by an equivalent resistor, Req.

## Slide 55: Series circuit and Voltage division
In a series circuit the current flows through each element is same.
But the supplied voltage is divided across the elements connected in series.
The total resistance is equal to sum of the individual resistances.
“The equivalent resistance of any number of resistors connected in series is the sum of the individual resistances.”

## Slide 56: Series circuit and Voltage division
V1=i*R1 , V2=i*R2 and V=V1+V2
i=V/(R1+R2)
V1={V/(R1+R2)}*R1
V2={V/(R1+R2)}*R2
If R1>R2 then, V1>V2
If R2>R2 then, V2>V1
If R1=R2 then, V1=V2

## Slide 57: Parallel circuit and Current division
Voltage across each element in a parallel connection is same.
V=V1=V2
At node a applying
KCL, i=i1+i2
V/Req=V1/R1+V2/R2
1
1
1
2
2
2

## Slide 58: Parallel circuit and Current division
V/Req=V1/R1+V2/R2
V/Req=V/R1+V/R2
1/Req=1/R1+1/R2
The equivalent resistance of two parallel resistors is equal to the reciprocal of the sum of the reciprocal of individual resistances.

## Slide 59: Parallel circuit and Current division
In a parallel circuit the potential differences across each element is same.
But the total current is divided into individual currents of the elements at the node or junction.

## Slide 60: Parallel circuit and Current division
Req=R2=0 ohm
Req=R1 ohm